UPDATE OF COST ESTIMATIONS FOR LCP

Questionnaire for improving the definition of operating costs

EGTEI secretariat

4 April 2012

CONTENT

1	Introduction	4

2	Desulphurisation techniques	5

2.1	Desulphurisation by LSFO (Limestone forced oxidation)	5

2.1.1	Reagent consumption	5

2.1.2	Industrial water consumption	5

2.1.3	By-product production	5

2.1.4	Electricity consumption	6

2.1.5	Labour Intensity	6

2.1.6	Fixed operating costs	6

2.2	Desulphurisation by LSNO (Limestone natural oxidation)	7

2.2.1	Reagent consumption	7

2.2.2	Industrial water consumption	7

2.2.3	By-product production	7

2.2.4	Electricity consumption	7

2.2.5	Labour Intensity	7

2.2.6	Fixed operating costs	8

2.3	Desulphurisation by spray dry scrubber	8

2.3.1	Reagent consumption	8

2.3.2	Industrial water consumption	8

2.3.3	By-product production	8

2.3.4	Electricity consumption	8

2.3.5	Labour Intensity	9

2.3.6	Fixed operating costs	9

2.4	Desulphurisation by furnace sorbent injection or duct sorbent injection	9

2.4.1	Reagent consumption	9

2.4.2	By-product production	9

2.4.3	Electricity consumption	10

2.4.4	Labour Intensity	10

2.4.5	Fixed operating costs	10

3	DeNOX techniques	11

3.1	Low NOx Burners	11

3.1.1	Combustion of fossil fuels in boilers	11

3.1.2	Combustion of fossil fuels in gas turbines	11

3.2	Selective Catalytic Reduction	11

3.2.1	Unit and catalyst layout	11

3.2.2	Average design operating data	12

3.2.3	Installation complexity	12

3.3	Selective Non-Catalytic Reduction	13

3.3.1	Average design operating data	13

3.4	Common Parameters	13

3.4.1	Labour Intensity	13

3.4.2	Fixed operating costs	13

4	Reduction of PM	14

4.1	Efficiency and achievable ELVs	14

4.2	Electricity consumption	14

4.3	Bag lifetime	15

4.4	Solid wastes	15

4.5	Common Parameters	15

4.5.1	Labour Intensity	15

4.5.2	Fixed operating costs	15

# Introduction

This document is an extract of the document prepared for the meeting of the EGTEI sub group for the update of cost estimations of reduction techniques for LCP, of 31 January 2012. It has been completed with techniques missing in the previous document.

It was expressed by the participants to the meeting that the documents were not easy to use and answer questions.

Consequently, the secretariat has elaborated this questionnaire which summarizes the questions presented previously. According to the cases, validation of some hypothesis is also expected.

Please could you answer the questions or validate the data of the secretariat if you think they are correct.

For your information the EGTEI secretariat is considering the following techniques for LCPs larger than 50 MWth.

| DeSOx | Wet FGD : limestone forced oxidation |
| --- | --- |
|  | Wet FGD : limestone natural oxidation |
|  | FGD by furnace sorbent injection |
|  | FGD by dry duct sorbent injection |
|  | FGD by using spray dry scrubber |
|  | Low sulphur fuels |
| DeNOx | Low NOx burner first generation (600 - 800 mg/Nm3) |
| Boiler | Low NOx burner second generation (400 - 600 mg/Nm3) |
|  | Low NOx burner third generation (300 - 400 mg/Nm3) |
|  | Flue gas recirculation |
|  | Selective Non-Catalytic Reduction |
|  | Selective Catalytic Reduction |
| Dust | Electrostatic Precipitators ESP |
|  | Fabric Filters (FF) |
| DeNOx | DLN |
| Turbine | Water injection |
|  | Steam injection |

Fuels considered are :

- Hard coal, brown coal,

- Heavy fuels, medium distillates,

- Natural gas,

- Biomass wood cofired with coal.

# Desulphurisation techniques

## Desulphurisation by LSFO (Limestone forced oxidation)

### Reagent consumption

What is average limestone purity? 95 to 97 %, 100 %? Please specify.

What is the average limestone consumption according to the efficiency required?

| Efficiency of SO2 removal η | t CaCO3/t SO2 abated | Ratio Ca/S |
| --- | --- | --- |
| 85.0% |  |  |
| 90.0% |  |  |
| 95.0% |  |  |
| 98,0% |  |  |

What are prices of limestone in 2011? Please specify for which country.

The secretariat has the following data.

| Efficiency of SO2 removal η | t CaCO3/t SO2 abated | Ratio Ca/S |
| --- | --- | --- |
| 85.0% | 1.41 | 0.90 |
| 90.0% | 1.48 | 0.95 |
| 95.0% | 1.59 | 1.02 |

Or

| Efficiency of SO2 removal η | t CaCO3/t SO2 | Ratio Ca/S |
| --- | --- | --- |
| 85.0% | 1.48 | 0.95 |
| 90.0% | 1.56 | 1.00 |
| 95.0% | 1.67 | 1.07 |

### Industrial water consumption

What are common CaCO3 concentrations used? 15 to 20 % solids? More? Please specify.

What are volumes of water to be added to compensate losses and purges in case of LSFO?

What are prices of industrial water in 2011? Please specify for which country.

### By-product production

What are prices of gypsum sold in 2011? Please specify if there are conditions associated, the country for which the costs are provided.

What are prices of waste disposal in 2011? Please specify if there are conditions, the country for which the costs are provided.

### Electricity consumption

What is the electricity consumption expressed in % of the gross electricity power production or in kWh/MWth full load according to the sulphur content of fuel and efficiency of the LSFO? Please provide information with as much details as possible. If you have other types of information, please do not hesitate to provide it.

What are prices of electricity? Please specify for which country.

The secretariat has the following information:

According to reference [4] for a coal with 1.3 % S and a desulphurisation efficiency of 98 % for an unit of 500 MWe, auxiliary power for fans to overcome system pressure drop, caused by the flue gas flow through the absorber and other auxiliary equipment such as mist eliminator, is 5.46 MW for a total pressure drop of 0.2 m water column, in a LSFO. This gives 1.1 % of the net electricity production of the unit.

Reference [5] provides 1.1% of the net generation for a coal with a sulphur content of about 1 % and 1.5 % for a coal with a sulphur content of 2.25 % for a LSFO. The FGD efficiency is not provided. For a FSNO, it is 1 % instead of 1.5%.

Reference [10] provides auxiliary power of 10 to 12 MW for a unit of 600 MWe and a deSOx efficiency of 90 % for a LSFO.

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size?

What is the demand for operators, in man-year for different size plants?

| Demand in man-year | LSFO |
| --- | --- |
| Small Combustion Plant (< 100 MWth) |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |
| Large Combustion Plant (> 500 MWth) |  |

What are prices of human resources in €/man-year? Please specify for which country.

The following data are available:

12 operators (40 hours / week) are needed for an FGD control in an existing plant according to reference [4] but 8 on a new plant. Reference [10] provides 10 operators for a 600 MWe. According to the reference 8 the need is constant whatever the size is. However this need has to be checked for power plant between 50 to 100 MWth or a little bit more.

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly? Have you other information? If you provide other percentages, please could you specify what you include?

## Desulphurisation by LSNO (Limestone natural oxidation)

### Reagent consumption

What is average limestone purity? 95 to 97 %, 100 %? Please specify.

What is the average limestone consumption according to the efficiency required?

| Efficiency of SO2 removal η | t CaCO3/t SO2 abated | Ratio Ca/S |
| --- | --- | --- |
| 85.0% |  |  |
| 90.0% |  |  |
| 95.0% |  |  |
| 98,0% |  |  |

What are prices of limestone in 2011?

### Industrial water consumption

What are common CaCO3 concentrations used? 15 to 20 % solids? More? Please specify.

What are volumes of water to be added to compensate losses and purges in case of LSFO?

What are prices of industrial water in 2011? Please specify for which country.

### By-product production

What are prices of gypsum sold in 2011? Please specify if there are conditions, the country for which the costs are provided.

What are prices of waste disposal in 2011? Please specify if there are conditions, the country for which the costs are provided.

### Electricity consumption

What is the electricity consumption expressed in % of the gross electricity power production or in kWh/MWth full load according to the sulphur content of fuel and efficiency of the LSFO? Please provide information with as much details as possible. If you have other types of information, please do not hesitate to provide it.

What are prices of electricity? Please specify for which country.

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size?

What is the demand for operators, in man-year for different size plants?

| Demand in man-year | LSNO |
| --- | --- |
| Small Combustion Plant (< 100 MWth) |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |
| Large Combustion Plant (> 500 MWth) |  |

What are prices of human resources in €/man-year? Please specify for which country.

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly? Have you other information? If you provide other percentages, please could you specify what you include?

## Desulphurisation by spray dry scrubber

### Reagent consumption

What is the most used reagent? Lime, limestone, another alkaline reagent? Please specify for what reagent you provide information.

What is the average reagent consumption according to the efficiency required?

| Efficiency of SO2 removal η | t reagent/t SO2 abated |
| --- | --- |
| 85.0% |  |
| 90.0% |  |
| 95.0% |  |
| 98,0% |  |

What are prices of the reagent in 2011? Please specify for which country.

### Industrial water consumption

What are common reagent concentrations used? 15 to 20 % solids? More? Please specify.

What are volumes of water to be added to compensate losses and purges?

What are prices of industrial water in 2011? Please specify for which country.

### By-product production

What is the use of byproduct? Can they be recovered or are they considered as a waste?

What are prices of recovered products sold in 2011? Please specify if there are conditions.

What are prices of waste disposal in 2011? Please specify if there are conditions.

### Electricity consumption

What is the electricity consumption expressed in % of the gross electricity power production or in kWh/MWth full load according to the sulphur content of fuel and efficiency of technique? Please provide information with as much details as possible. If you have other types of information, please do not hesitate to provide it.

What are prices of electricity? Please specify for which country.

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size?

What is the demand for operators, in man-year for different size plants?

| Demand in man-year | Spray dry scrubber |
| --- | --- |
| Small Combustion Plant (< 100 MWth) |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |
| Large Combustion Plant (> 500 MWth) |  |

What are prices of human resources in €/man-year? Please specify for which country.

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly? Have you other information? If you provide other percentages, please could you specify what you include?

## Desulphurisation by furnace sorbent injection or duct sorbent injection

### Reagent consumption

What is the most used sorbent? Lime, limestone, another alkaline reagent?

Please specify for what sorbent you provide information.

What is the average sorbent consumption according to the efficiency required?

| Efficiency of SO2 removal η | t sorbent/t SO2 abated |
| --- | --- |
| 85.0% |  |
| 90.0% |  |
| 95.0% |  |
| 98,0% |  |

What are prices of the sorbent in 2011? Please specify for which country.

### By-product production

What is the use of byproducts? Can they be recovered or are they considered as a waste?

What are prices of recovered products sold in 2011? Please specify if there are conditions associated, the country for which the costs are provided.

What are prices of waste disposal in 2011? Please specify if there are conditions associated, the country for which the costs are provided.

### Electricity consumption

What is the electricity consumption expressed in % of the gross electricity power production or in kWh/MWth full load according to the sulphur content of fuel and efficiency of the technique? Please provide information with as much details as possible. If you have other types of information, please do not hesitate to provide it.

What are prices of electricity? Please specify for which country.

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size?

What is the demand for operators, in man-year for different size plants?

| Demand in man-year | Dry absorption |
| --- | --- |
| Small Combustion Plant (< 100 MWth) |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |
| Large Combustion Plant (> 500 MWth) |  |

What are prices of human resources in €/man-year? Please specify for which country.

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly? Have you other information? If you provide other percentages, please could you specify what you include?

# DeNOX techniques

## Low NOx Burners

### Combustion of fossil fuels in boilers

Which emission levels can be achieved with low NOx burners? We would like to distinguish between up to three “generations”, as achievable boiler outlet concentrations have changed since the 1990ies.

New coal plants are expected to be mainly tangentially-fired dry bottom boilers. Biomass co-firing is not taken into account at this level. Fuel Oil is assumed to be heavy fuel oil or medium distillate fuel oil.

| Boiler Outlet Emission Level (mg NOx/Nm³ at 6% O2) | Hard Coal | Lignite | Fuel Oil | Natural Gas |
| --- | --- | --- | --- | --- |
| “New generation” LNBs (roughly after 2005) |  |  |  |  |
| “Middle generation” LNBs (roughly between 1995-2005) |  |  |  |  |
| “Old generation” LNBs (roughly < 1995) |  |  |  |  |

The secretariat has been working with the following data, assembled from literature reviews:

| Boiler Outlet Emission Level (mg NOx/Nm³ at 6% O2) | Hard Coal | Lignite | Fuel Oil | Natural Gas |
| --- | --- | --- | --- | --- |
| “New generation” LNBs (roughly after 2005) | 300-400 | ~150 | No appropriate data could be found | No appropriate data could be found |
| “Middle generation” LNBs (roughly between 1995-2005) | 400-550 | ~200 |  |  |
| “Old generation” LNBs (roughly < 1995) | 500-700 | ~300 |  |  |

### Combustion of fossil fuels in gas turbines

Which emission levels can be achieved at gas turbines? Herein, liquid fuels are assumed to be diesel or other very low sulphur fuel.

| Turbine Outlet Emission Level (mg NOx/Nm³ at 15% O2) | Liquid Fuels | Natural Gas |
| --- | --- | --- |
| Gas Turbine w/o further NOx treatment |  |  |
| GT with water injection |  |  |
| GT with steam injection |  |  |
| DLN GT |  |  |

Up to now, the secretariat has not worked on the field of gas turbines. Therefore, no detailed data has been collected.

## Selective Catalytic Reduction

### Unit and catalyst layout

The following assumptions have been made throughout the last years to reflect the most commonly used type of SCR installation. If this is not reflecting the most commonly used type, please indicate.

- High dust installation at the boiler outlet / gas turbine outlet

- For solid fuels, 3+1 layers are used. Due to lack of differing data, this will be assumed for all other cases as well.

- Ammonia is the reference reducing agent, injected as aqueous ammonia (mostly at ~20-30% wt.)

The secretariat has not been able to collect much data and knowledge on specific catalyst volume needs. The only figure obtained was 0.32 m³/MWth boiler capacity for a hard coal fired unit. Very old data was 0.5 m³/MWth for solid and 0.11 m³/MWth for liquid and gaseous fuels.

### Average design operating data

The aim of our work is to characterise an average SCR operation. Therefore following parameters are used:

| Average SCR Efficiency | [%] | Average Efficiency during a full regeneration cycle of the total (3+1) unit. |
| --- | --- | --- |
| Average NH3/NOx Ratio | [moles NH3in / mole NOxin] | NH3 Injection per NOx inlet |
| Average Catalyst Lifetime between Regeneration | [operating hours] | With assumed “typical” catalyst management strategies. No biomass co-firing. |
| Average Number of Regeneration Cycles | [number] |  |
| Average Unit Power Consumption | [MWh/Mio. Nm³ treated] | Pressure Drop, Mixing and Injection with reference to 1 Mio. Nm³ flue gas. |

It is assumed that the NH3 slip is in line with the corresponding European legislations.

With reference to literature and interviews [6]-[8], [10], [12]-[14], the secretariat has collected the following figures, characterizing a “typical” hard coal fired power plant. Due to lack of data, a similar behaviour for all other fuels is assumed.

| Average SCR Efficiency | 85-90% | Average Efficiency during a full regeneration cycle of the total (3+1) unit. |
| --- | --- | --- |
| Average NH3/NOx Ratio | 0.85 | NH3 Injection per NOx inlet |
| Average Catalyst Lifetime between Regeneration | 15.000 h | With assumed “typical” catalyst management strategies. No biomass co-firing. |
| Average Number of Regeneration Cycles | 5? |  |
| Average Unit Power Consumption | 0.3% of gross electrical output | Pressure Drop, Mixing and Injection with reference to 1 Mio. Nm³ flue gas. |

### Installation complexity

What are typical reasons for increasing installation complexity (especially for retrofitting) and increasing costs above average levels? Up to now, the following reasons have been collected with strong influence on total installation costs of an SCR:

- Economizer splitting / moving needed

- Space requirements for retrofits

- Installation near the seaside (more corrosion-resistive construction steel needed)

## Selective Non-Catalytic Reduction

### Average design operating data

The aim of our work is to characterise an average SNCR operation. Therefore following parameters are used:

| Average SNCR Efficiency | [%] |  |
| --- | --- | --- |
| Average NH3/NOx Ratio | [moles NH3in / mole NOxin] | Alternatively urea/NOx Ratio |
| Average Unit Power Consumption | [MWh/Mio. Nm³ treated] | Mixing and Injection with reference to 1 Mio. Nm³ flue gas. |

It is assumed that the NH3 slip is in line with the corresponding European legislations.

With reference to literature, the secretariat has collected the following figures, characterizing a “typical” hard coal fired power plant. Due to lack of data, a similar behaviour for all other fuels is assumed.

| Average SNCR Efficiency | 25-40% |  |
| --- | --- | --- |
| Average NH3/NOx Ratio | No appropriate data could be found | Alternatively urea/NOx Ratio |
| Average Unit Power Consumption |  | Mixing and Injection with reference to 1 Mio. Nm³ flue gas. |

## Common Parameters

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size, i. e. if the operation of a SCR for a 100 MWe plant is less operator-intensive than the operation of a SCR for a 900 MWe plant.

|  | SCR | SNCR |
| --- | --- | --- |
| Small Combustion Plant (< 100 MWth) |  |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |  |
| Large Combustion Plant (> 500 MWth) |  |  |

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly?

# Reduction of PM

## Efficiency and achievable ELVs

Are data in this table indicating ELVs achievable with the use of fabric filters (FF) or electrostatic precipitators (ESP) for solid fossil fuels correct?

| ELV | 10 mg/Nm3 | 20 mg/Nm3 | 30 mg/Nm3 | 50 mg/Nm3 |
| --- | --- | --- | --- | --- |
| FF | y | y | y | y |
| 2 fields ESP | n | n | With FGD? | With FGD? |
| 3 fields ESP | n | With FGD? | y | y |
| 4 fields ESP | ? | y | y | y |
| 6 fields ESP | y | y | y | y |

## Electricity consumption

In order to determine the electricity demand, indicators are necessary. Could you provide information?

These indicators could be the pressure drop and the power needed for electrodes and bag cleaning.

- What is the pressure drop for ESP and FF according to different efficiency?

- Power needed for electrodes and pulse jet cleaning according to the size of combustion units and PM concentrations to be obtained?

or

- What is the electricity consumption per MWth for different efficiency or ELVs to be obtained (10, 20, 30 or 50 mg/Nm3)? For coal and heavy fuel oil?

The secretariat has the following information:

| Solid fuels | FF | ESP |
| --- | --- | --- |
|  | Pressure drop mbar | Power for pulse jet cleaning | Pressure drop mbar | Power for electrodes |
| 5 mg/Nm3 | 10 to 12 | 1360 kW for a 800 MWe burning coal | 3 to 4 | 1060 kW for a 800 MWe burning coal |
| 10 mg/Nm3 | ? | ? | ? | ? |
| 20 mg/Nm3 | ? | ? | ? | ? |

Deduster 4 in this table can be an ESP or a FF, it is an average value.

|  | Achieved concentration [mg/Nm3] | Electricity consumption [GWh/PJ] |
| --- | --- | --- |
| For solid fuel |
| Deduster 1 | 300 | 0.11 |
| Deduster 2 | 100 | 0.15 |
| Deduster 3 | 45 | 0.18 |
| Deduster 4 | 20 | 0.2 |
| For liquid fuel |
| Deduster 1 | 5 | 0.1 |

## Bag lifetime

What is the bag lifetime? 20 000 to 30 000 hours? Please specify the nature of bags for which lifetime is provided.

## Solid wastes

What is done with dust recovered (waste disposal, recovery)? Please specify according to the case (ESP directly after a boiler or after a dry or semi dry FGD)?

Prices of waste disposal or dust sold? Please specify for which country.

## Common Parameters

### Labour Intensity

In order to determine the labour demand of operating the plant, indicators are necessary, which state the average man-year workload of operating such flue gas treatment units.

Furthermore, the question has been raised, to what such workload is depending on the plant size?.

|  | FF | ESP |
| --- | --- | --- |
| Small Combustion Plant (< 100 MWth) |  |  |
| Medium Sized Combustion Plant (100-500 MWth) |  |  |
| Large Combustion Plant (> 500 MWth) |  |  |

### Fixed operating costs

The fixed operating costs include costs of maintenance and repair, insurance, administrative overhead, etc. Taxes are not included in order to be coherent with GAINS.

Currently, 4% of total investment is assumed to be an appropriate estimate for these costs. Does this estimate meet real figures roughly? What is your estimation? Please specify what you include in fixed operating costs.

REFERENCES used to determine costs

- EIPPCB – Economics and cross media effects - http://eippcb.jrc.es/reference/ecm.html

- EIPPCB - LCP BREF

- EGTEI methodology 2005

- National lime association - Wet flue gas desulphurisation technology evaluation –– January 2003

- IEA coal research – The clean Coal centre – Air pollution control costs for coal fired power stations – 2001

- R Brandwood – EGTEI UNECE abatement cost report – 2008

- H. Nalbandian – Economics of retrofit air pollution control technologies – IEA CCC report 2006

- EGTEI – Simon Schulte – determination of costs for activities of annexes IV, V and VII – sectors: Boilers and process heaters

- MG Milobowski – Babcock and Wilcox - Wet FGD system material cost update – 1997

- Information provided by one expert in EDF on the 17 january 2012

- H. C. Frey, L. Tran – Quantitative Analysis of Variability and Uncertainty in Environmental Data and Models – Performance, Emissions, and Cost of Combustion-Based NOx Controls for Wall and Tangential Furnace Coal Fired Power Plants – Vol. 2 – Raleigh, 1999.

- W. Ellison, H. Weiler, R. McIlvaine – Germany Power Industry Advisory for SCR Operational Success in U.S. High Sulfur Applications – The Clearwater Coal Conference, Clearwater – 2003.

- B. Heiting – State of the art of flue gas cleaning in large power plants – VGB PowerTech – 06/2011 – pp. 114-123.

- P. Forzatto: Present status and perspectives in de-NOx SCR catalysis – Applied Catalysis A – 222 (2001) – pp. 221-236.

- US EPA – Air Pollution Cost Manual – Washington D.C. – 2002.

- F. Van Aart (KEMA, NL) – Comments for the kick off meeting

- EPA - CUECost workbook development documentation version 5 - 2009

# Footnotes

Working document for the meeting of 31 January 2012. Update of cost estimation for LCP. EGTEI secretariat. 20 January 2012